## Slide 1: Understanding Proteomics

## Slide 2: Why study Proteomics?
Human Genome Project found fewer protein-coding genes in the human genome than proteins in the human proteome
(i.e.) 20,000 to 25,000 genes coding for
about 50,000 proteins.

## Slide 3: Problem?
Protein diversity cannot be fully characterized by gene expression analysis, thus proteomics is useful for characterizing cells and tissues

## Slide 4: Why perform Proteomics ?
Most proteins function in collaboration with other proteins, and one goal of proteomics is to identify which proteins interact.
This often gives important clues about the functions of newly discovered proteins

## Slide 5
How does it work?
Proteins are resolved, sometimes on a massive scale. Protein separation can be performed using 2-D gel electrophoresis,
  `usually separates proteins first by isoelectric point and then by molecular weight.
Once proteins are separated and quantified, they are identified
Individual spots are cut out of the gel and cleaved into peptides with proteolytic enzymes

## Slide 6
These peptides can then be identified by mass spectrometry,
Specifically: matrix-assisted laser desorption-ionization time-of-flight (MALDI-TOF) mass spectrometry.
In this procedure, a peptide is placed on a matrix, which causes the peptide to form crystals.

## Slide 7
Then the peptide on the matrix is ionized with a laser beam and an increase in voltage at the matrix is used to shoot the ions toward a detector in which the time it takes an ion to reach the detector depends on its mass.
The higher the mass, the longer the time of flight of the ion.

## Slide 8
In a MALDI-TOF mass spectrometer, the ions can also be deflected with an electrostatic reflector that also focuses the ion beam.
Thus, the masses of the ions reaching the second detector can be determined with high precision and these masses can reveal the exact chemical compositions of the peptides, and therefore their identities!

## Slide 9
Protein mixtures can also be analyzed without prior separation.
These procedures begin with proteolytic digestion of the proteins in a complex mixture
The resulting peptides are often injected onto a high pressure liquid chromatography column (HPLC) that separates peptides based on hydrophobicity.
HPLC can be coupled directly to a time-of-flight mass spectrometer using electrospray ionization

## Slide 10
electrospray ionization: A technique used in mass spectrometry to produce ions.
It is especially useful in producing ions from macromolecules because it overcomes the propensity of these molecules to fragment when ionized

## Slide 11
Peptides eluting from the column can be identified by tandem mass spectrometry (MS/MS).
The first stage of tandem MS/MS isolates individual peptide ions, and the second breaks the peptides into fragments and uses the fragmentation pattern to determine their amino acid sequences.
Labeling with isotope tags can be used to quantitatively compare proteins concentration among two or more protein samples.

## Slide 12
Finally, use databases.
Computer compares sequences to other sequences stored in an internationally accessible database.
Determines the identity of the isolated protein
As the entire human genome is known, computers are able to determine nearly every potential protein.
New proteins are “discovered” when they match sequences predicted by the computer that have not previously been found.

## Slide 13: How to interpret data?